## Slide 1: TRACLabs Background
Established January 1997
Location: Houston Texas, near NASA Johnson Space Center
Purpose: Conducting world-class research in Automation and Robotics, with the mission to develop new technologies and products for emerging markets
20 full-time scientists and engineers

## Slide 2: Research Areas
Decision Support
  Task execution assistance
  System modeling
  Task planning
  Data summarization
Robotics
  Dexterous manipulation
  Perception
  Mobile robot navigation
  Operator interfaces
  Challenges
    4th Place 2013 DARPA VRC
    6th Place 2013 DARPA DRC Trials
    9th Place 2015 DARPA DRC Finals

## Slide 3: Manipulation Research Problem
DARPA Robotics Challenge and NASA humanoids needed to use tools, manipulate objects, and interact with complex environments.
  Turning valves; using drills; walking over uneven terrain
MoveIt! is great for pick and place and avoiding obstacles, but lacks some of the technologies needed for robustly teleoperating humanoid robots performing the tasks above.

## Slide 4: CRAFTSMAN
CRAFTSMAN is a NASA funded project that looks to integrate and generalize some of our DRC technologies into a ROS-compatible software suite that works for arbitrary robots.
Current CRAFTSMAN software suite:
  TRAC-IK: Inverse Kinematics
  Robot Interaction Tools: 3D Visualization/User Interface tools
  Affordance Templates: process/task definition libraries

## Slide 5: Improving Open Source IK
Iterative Inverse Jacobian methods suffer from a variety of issues:
  Cannot handle joint limits
    Some tricks can be done but do not fully handle all scenarios
  Cannot handle tolerances in goals
    Tolerances can be used each iteration to CHECK for success, but don’t inform the search.
  Typically a single solution is found

## Slide 6: TRAC-IK https://bitbucket.org/traclabs/trac_ik

## Slide 7: Additional Improvements
Publicly Released
  Multiple solutions found if desired
  Condition metrics used for sorting solutions
    Manipulability; Min Distance from seed; Speed
  Joints can be “frozen” when desired
  Arbitrary end effector position/orientation constraints
  MoveIt! Plugin available
Private (soon to be released)
  Collision detection for robot self collisions pushed into IK
  1KHz collision-free Cartesian trajectories

## Slide 8: Robot Interaction Tools
Teleoperation Environment
  Rviz front end to TRACLabs’ planners, TRAC-IK, and MoveIt! that provides the remote operator with improved situational awareness and commanding capabilities.

## Slide 9: Robot Interaction Tools example
Video: https://www.youtube.com/watch?v=COpq03PHdi8

## Slide 10: Affordance Templates
Interactive 3D task programming & execution framework
  inherent generalization across robots, tasks, & environments
  used on Robonaut 2, Valkyrie, Atlas, PR2, and Fetch
Supports different levels of shared & full autonomy
Intuitive graphical tools to set task parameters and get feedback from the robot
task transferability
between robots
adjustable to
task context

## Slide 11: Opening Door Template
Video: https://www.youtube.com/watch?v=kYhJDx1wuuA

## Slide 12: Mobility Templates
Video: https://www.youtube.com/watch?v=0Nbr5-ooBo4

## Slide 13: NASA Habitat Demo
Video: https://www.youtube.com/watch?v=wf5a-HLw8Zk

## Slide 14: Future Work
Adding force/impedance control to CRAFTSMAN
  Support for reactive control
  How to visualize commands in Rviz
Task conditioning metrics for TRAC-IK
  “Achieve best initial configuration for using screw driver.”
Sorting IK by maximum obstacle distance
  Avoiding obstacles as much as possible
Stance planning for best manipulator performance for tasks
Perceptual registration of object templates to sensory data

## Slide 15: Thank You